## Slide 1: Final Assignment Project Plan
Kevin Berg ENGR 103

## Slide 2: Overall Project Overview
We will detect steps and/or vibrations
  Vibration sensor connected to ESP board #1
  ESP #1 will interpret sensor data to identify steps
  When a step is detected, a command will be output to a PHP form
  The PHP webpage will interpret the command and output an on/off command to a text file
  ESP #2 will get the command from the text file
  Depending on the command, ESP #2 will output a specific LED behavior

## Slide 4: My Project Overview – PHP Webpage
The PHP Webpage will receive POST data from the ESP board #1
  The PHP webpage does not verify the data received
    Fault detection of the output command is done by ESP32 board #2
The PHP Webpage copies the POST data to a text file
  Text file is on the ENGR webspace
  Data in the text file is overwritten each time

## Slide 5: My Project Overview – ESP32 Program
My program will connect to WiFi and the ENGR webspace
  The program will get text from a specified text file
    The text file is created by the PHP webpage based off of the output from ESP board #1
  The program will interpret the text based off expected inputs
    A fault will be output via the LED and serial monitor if the text does not meet expectations
    A command is generated from the text
  The program will activate an LED based off the command
  The program will delay for 5 seconds, then restart
  If the same command is received for 2 consecutive checks (about 10 seconds)
    A different response will be generated

## Slide 6: My Project Picture
Input from Text File
ESP32 Board #2
ENGR Webspace
Output: LED Light
Input from ESP Board #1
PHP Webpage
Output: Text File
Program restarts every 5 seconds

## Slide 7: Program Inputs – PHP Webpage
Command input from ESP32 board #1
  Expected commands are “on” or “off”

## Slide 8: Program Inputs – ESP32 Program
Text from ENGR webspace page
  This will be the only input to the program
  The text will be compared to expected text inputs
  An output will be determined based on the text input

## Slide 9: Program Outputs – PHP Webpage
The webpage copies the text received in the form POST data labeled “command” to a text file
  The file is named “finalassignmenttest.txt”
  The file is overwritten each time it is updated by the PHP website

## Slide 10: Program Outputs – ESP32 Program
The program will control output to an RGB LED and the serial monitor
  If the program receives a new “on” command, it will turn on solid green.
    The program will also output the command text via the serial monitor.
  If the program receives a new “off” command, it will turn on solid red.
    The program will also output the command text via the serial monitor.
  If the program does not receive a new command after 10 seconds, it will flash the blue at 1 Hz.
    The program will also output text to the serial monitor indicating that it has not received a new command.
  If the program receives an invalid text input, cannot connect to WiFi or the webpage, it will flash the red LED at 1 Hz
    An error message will also be output to the serial monitor.

## Slide 11: Test Plan Page 1
Program receives “on” text from the ENGR text file
  Green LED turns on solid
  Blue LED will start flashing at 1 Hz if no other command is received after 10 seconds
Program receives “off” text from the ENGR text file
  All LEDs turn off
  Blue LED will start flashing at 1 Hz if no other command is received after 10 seconds
ESP cannot connect to WiFi
  The red LED will flash at 5 Hz
  A “Waiting for WiFi connection” message is output over the serial monitor
  The program will continue to try to connect to WiFi

## Slide 12: Test Plan Page 2
ESP receives an HTML error
  The red LED will flash at 1 Hz
  An error message will be output to the serial monitor
    Message should include HTML error code
ESP receives unexpected text from the webpage
  The red LED will flash at 1 Hz
  An error message, including the received text, will be output to the serial monitor

## Slide 13: Program Steps – PHP Webpage
Command is sent from ESP32 board #1
Expected format is “command=…”
If the received text is not in the expected format
An error will be printed on the webpage
If the received test is in the expected format
Any text after “command=“ is
Output to a text
file
Program restarts when a new input is received from ESP32 board #1

## Slide 14: Program Steps – ESP32
Connect to WiFi
Output an error
If unable to connect
Get text from ENGR webspace
Output an error
If text is invalid
Compare input text to expected inputs
If text indicates an “on” command
If text indicates an “off” command
If the command has not changed
Turn the green LED on solid
Turn the red LED on solid
Add 1 to repeat count
Print “on”
Command on serial monitor
Print “off”
Command on serial monitor
Print “waiting”
on serial monitor
Repeat count = 0
Wait 5 seconds
Wait 5 seconds
Repeat count = 0
Wait 5 seconds
If repeat count ≥ 1
Flash blue LED at 1 Hz