## Slide 1
Key Components:
Force Mechanism→Sensor→MC→DB→Data Presentation
Force Mechanism - Hinge mechanism that bird interacts with to collect food reward. Resistive force determined changeable by variable force spring. Includes safety system to protect the birds.
Sensor - A load cell and amplifier that takes data (10 samples/sec) on the force applied to the force mechanism, which is sent to the microcontroller.
Microcontroller (MC) - Receives data from the force sensor and sends this data to the database wirelessly. Able to connect to secure and unsecure networks.
Database (DB) - MySQL database is used to manage the data collected from the load cell.
Data Presentation - PHP website using the chart.js API to display data as a graph.
Next Steps
While the solution built fulfills the main purpose of the project; to measure and record data on force applied by the birds; there is still room for improvement in terms of the usage as well as the system itself. Ideally, 30 - 40 individual systems with differing resistive forces could be used in a proposed experiment to study behavior. Our system currently is designed to be used individually, as it requires its own microcontroller and power supply. To adapt our system for mass use, it could be modified to utilize a battery pack for power. Furthermore, rather than each system using its own microcontroller, the system could be designed to easily attach to a main microcontroller, that allows for multiplie systems to take data.
Background and Summary
The purpose of this project is to provide a foraging puzzle that will measure the force produced by the red crossbill (Loxia curvirostra) while it forages for seed. The physical device will hang from the side of a cage and apply a variable force to a hinge that the birds will open for seeds. The force produced will be then examined to determine different feeding behaviors in risk-reward scenarios and how willing they are to work for food. The goal of this project is to find a way to accurately measure the force produced by the red crossbill so the information can be used for research purposes.
Foraging Puzzle for Songbirds
Researching foraging methods & behavior
Project Team
ECE.09
Michael Austin Crockett
crocketm@oregonstate.edu
Variable Force Mechanism
Enclosure
Brieanna Jeibmann
JeibmanB@oregonstate.edu
Voltage Regulator
PCB Design
Engineering Requirements
Measure Force
Safety for the Birds
Data Visualization
Cleanability of System
Damage Resilient
Mounting to Side of Cage
Bird Accessibility
Budget
Shengmei Hu
hushe@oregonstate.edu
Force Sensor
Main Code
Bradley Martin
martbrad@oregonstate.edu
Database
Data Presentation
Project Partner
Dr. Jamie Cornelius
Assistant Professor
cornelja@oregonstate.edu
Ecophysiologist interested in the mechanisms wild animals use to cope with unpredictable and extreme environmental events.
Figure 1: Foraging Bird
Figure 2: Block Diagram
Figure 3: Mechanical Drawing
Figure 4: Bird Testing