## Slide 1: Neurons for Neutrons: Preliminary Results of Predicting SMR Computation Load with Machine Learning
Alexander Mote, Lizhong Chen
The Center for Exascale Monte Carlo Neutron Transport (CEMeNT)
Oregon State University
October 6, 2022

## Slide 2: Summary
Domain decomposition is needed for Exascale computing, but current methods use “trial and error”
  Changes to subdomain allocation/input domain require new simulations
Machine Learning allows us to predict computation load, but necessitates a new optimization tool
  Represent domain data in a way that works for computer vision
  Train a CV model architecture on domain parameters
Results:
  Current machine learning model can predict SMR computation load on an arbitrary domain decomposition with 79% accuracy
  Model considers neutron transmission between subdomains and communication overhead
  CNN and MLP models have been developed; MLP network currently outperforms, but CNN has potential for further development

## Slide 3: Research Objectives
Optimize heterogenous hardware utilization on HPC systems
Develop domain decomposition techniques to enhance parallel performance
Use Machine Learning to optimize parameter tuning for hardware allocation

## Slide 4: Research Objectives
Optimize heterogenous hardware utilization on HPC systems
Develop domain decomposition techniques to enhance parallel performance
Use Machine Learning to optimize parameter tuning for hardware allocation

## Slide 5: Current Domain Decomposition Method
Subdomain Initialization
  Domain is divided into subdomains when input file is created
Small-Scale Simulation
  Analyze runtime of divided domain with 1 processor per subdomain
Processor Allocation
  Processors are assigned non-uniformly to balance workload
Image Source: Ellis et al., 2019

## Slide 6: Why Machine Learning?
Subdomain & resource allocation parameters are tuned manually
  Processors per task, subdomain creation, memory allocation, etc.
Small-scale simulations can take on the order of hours to run
  Must be repeated whenever any configuration settings change
Machine Learning for Domain Decomposition is promising
  Small-scale particle output can be approximated by a series of functions
  Our unique problem requires a unique optimization tool

## Slide 7: Creating a Model for Computation Load Prediction
Divide domain into N elementary spatial units
Create a vector v of computation-relevant data for each unit
  Element composition, domain boundaries, etc.
Divide the domain into S subdomains according to user input
  Assign each spatial unit to its subdomain
Add global parameters P from user input
  Number of particles, cycles, etc.
From these inputs, predict a computation load L for each subdomain
Image Source: Ellis et al., 2019
Example 3D Domain Decomposition

## Slide 8: Creating a Model for Computation Load Prediction
+


## Slide 9: Challenge/Solution 1: Fixed Input & Output Size
Shift simulations only provide particle data/computation information per subdomain
  Variable sized input/output; not good for computer vision algorithms
  Without a fixed input/output, separate models would have to be trained on each subdomain division
  Additionally, internal spatial data within subdomain is lost with Shift storage
Fixed Input: NxN matrix
  Preserves relationship between elementary domain units as well as subdomains
  Each row contains all units within a given subdomain
  Each column contains a single elementary domain unit vector
Fixed Output: N-element array
  Each element represents combined computational load of each subdomain
  Includes neutrons travelling between subdomains, and communication overhead

## Slide 10: Current Model Input View
Example: 32 subdomains (4x4x2 decomposition)

## Slide 11: Current Model Input View
Example: 32 subdomains (4x4x2 decomposition)

## Slide 12: Current Model Input View
Example: 32 subdomains (4x4x2 decomposition)
Input assigns 512 elementary spatial units to 32 rows based on each unit’s subdomain
  16 units per subdomain
Heatmap in this example indicates normalized number of particles held by each unit before simulation
  Particle numbers were estimated from small-scale SMR simulations with 512 subdomains

## Slide 13: Challenge/Solution 2: Generating Dataset
Generating input/output dataset for SMR subdomains is challenging
  Thousands of datapoints are required to train the model
  Each decomposition datapoint produces ~2GB of data  4 TB of total data
  Each datapoint requires ~40 minutes to simulate on Sierra  1,300 hours of total simulation time
New data may need to be generated as model evolves and improves
Solution: Synthetic Dataset
  Generated synthetic datapoints based on a small set of SMR simulations
  Allowed for faster dataset generation, easier model design iteration, and saved computing resources
  Data points can be generated that stress the model by simulating extreme/uncommon circumstances
  Currently simulates net transfer between subdomains and communication overhead

## Slide 14: Current Model Performance
Prediction accuracy decreases as number of subdomains increases
  Most datapoints have a smaller number of subdomains
  Model weights may need additional training at higher subdomain values
Overall Testing Set Accuracy: 79%
  1000 datapoints in testing set
Improving Accuracy
  Deeper network architecture
  Tuning custom loss functions
  Adding more features to dataset
Chart: Accuracy on a Random Data Sample
| 72 | 40 | 25 | 64 | 40 | 36 | 36 | 36 | 60 | 100 | 45 | 45 | 72 | 48 | 24 | 36 | 32 | 24 | 36 | 24 | 30 | 32 | 90 | 50 | 60 | 60 | 32 | 90 | 48 | 45 | 24 | 30 | 36 | 36 | 24 | 80 | 30 | 72 | 100 | 40 | 75 | 54 | 24 | 48 | 120 | 30 | 64 | 125 | 60 | 126
Accuracy | 0.77 | 0.7104 | 0.8804 | 0.714 | 0.7918 | 0.7282 | 0.8758 | 0.7363 | 0.7925 | 0.7117 | 0.7582 | 0.7477 | 0.7205 | 0.7126 | 0.8515 | 0.8117 | 0.7455 | 0.8544 | 0.769 | 0.8785 | 0.8519 | 0.8577 | 0.7146 | 0.7631 | 0.7877 | 0.7912 | 0.852 | 0.714 | 0.8289 | 0.7572 | 0.8745 | 0.87 | 0.7912 | 0.7315 | 0.8713 | 0.7083 | 0.688 | 0.6946 | 0.6888 | 0.693 | 0.6991 | 0.6974 | 0.6816 | 0.6988 | 0.6958 | 0.671 | 0.6746 | 0.6712 | 0.6767 | 0.6526

## Slide 15: Next Steps
Continue Development of the Machine Learning Model
  Implement additional input vector features and global parameters
  Generalize inputs from SMR to other reactor domains
  Investigate optimization opportunities in time-dependent simulation
  Use load prediction to generate optimal domain decompositions
Further Optimization Opportunities
  Lassen Scheduler Parameters
  GPU Memory Allocation/Access
  Neutron Transport Task Scheduling (CUDA)
  And More…

## Slide 16: Conclusion
Subdomain computation load can be predicted by Machine Learning
Preliminary efforts have resulted in a model with a 79% prediction accuracy on SMR domains
MLP model currently performs best; however, CNN has more potential as additional input complexity is added

## Slide 17: Questions